## Slide 1
Unit III
(Part I)
Switching
Vinit R Tribhuvan
vrt22.comp@coep.ac.in
Notes: Data Communication

## Slide 2: Introduction
Whenever we have multiple devices, we have the problem of how to connect them to make one-to-one communication possible.
Solution : point-to-point connection between each pair of devices (a mesh topology) or between a central device and every other device (a star topology).
Solution is impractical and wasteful when applied to very large networks
  majority of those links would be idle most of the time
  number and length of the links require too much infrastructure
  Not cost effective
Notes: Data Communication

## Slide 3: Better Solution?
Switching
A switched network consists of a series of interlinked nodes, called switches.
Capable of creating temporary connections between two or more devices linked to the switch.
some of these nodes are connected to the end systems (computers or telephones) others are used only for routing.
Notes: Data Communication

## Slide 4: Three Methods of Switching
Traditionally, three methods of switching have been discussed:
  circuit switching
  packet switching
  message switching
Notes: Data Communication

## Slide 5: Circuit switching
A circuit-switched network consists of a set of switches connected by physical links.
Connection between two stations is a dedicated path made of one or more links.
Each connection uses only one dedicated channel on each link.
Each link is normally divided into n channels by using FDM or TDM

## Slide 7
When end system A needs to communicate with end system M, system A needs to request a connection to M that must be accepted by all switches as well as by M itself. This is called the setup phase.
After the dedicated path is established, the data-transfer phase can take place.

## Slide 8: Three phases
Circuit switching requires three phases:
  Setup phase
  Data Transfer phase
  Teardown phase

## Slide 9: Setup Phase
A dedicated circuit (combination of channels in links) needs to be established for two parties to communicate.
Connection setup means establishing dedicated channels between switches.
Switch I finds a channel between itself and switch IV
Switch I then sends the request to switch IV
Switch IV finds dedicated channel between itself and switch III
Switch III informs system M of system A’s intention at this time
An acknowledgment from system M is sent in the opposite direction to system A
After system A receives this acknowledgment is the connection established.

## Slide 10: Data-Transfer Phase
The two parties transfer the data in this phase

## Slide 11: Teardown Phase
When one of the parties needs to disconnect, a signal is sent to each switch to release the resources.

## Slide 12: Issues in Circuit Switching
Delay

## Slide 13: Delay
Delay is minimal
no waiting time at each switch
delay caused by the setup is the sum of four parts:
the propagation time of the source computer request (first slope)
the request signal transfer time (height of forst box)
the propagation time of the acknowledgment from the destination Computer (second slope)
the signal transfer time of the acknowledgment (height of second box)
The delay due to data transfer is the sum of two parts: the propagation time (slope of the colored box) and data transfer time (height of the colored box), which can be very long.

## Slide 14: Efficiency
Inefficient since resources are allocated during the entire duration of the connection.
resources are unavailable to other connections.
other connections are deprived of resources.

## Slide 15: Packet Switching
Message is divided into packets of fixed or variable size.
There is no resource allocation for a packet (bandwidth, processing time)
Packet is allocated on FCFS basis.
Two types of packet-switched networks:
  datagram networks
  virtual circuit networks

## Slide 16: Datagram networks
Packets in this approach are referred to as datagrams.
Each packet is treated independently of all others.
Datagram switching is normally done at the Network Layer.

## Slide 17: Datagram networks
All four packets (or datagrams) belong to the same message
Travel different paths to reach their destination.
Datagrams of transmission may arrive at their destination out of order with different delays between the packets. They may also be lost.
It is the responsibility of an upper-layer protocol to reorder the datagrams

## Slide 18: Routing Tables in Datagram Networks
Each switch (or packet switch) has a routing table which is based on the destination address.
The routing tables are dynamic and are updated periodically.
The destination addresses and the corresponding forwarding output ports are recorded in the tables.
It has a port dedicated for every destination address.

## Slide 19: Routing Tables in Datagram Networks
Every packet in a datagram network carries a header that contains
the destination address of the packet.
the switch receives the packet, this destination address is examined;
the routing table is consulted to find the corresponding port
through which the packet should be forwarded.
This address remains the same during the entire journey of the
packet

## Slide 20: Issues
Delay
greater delay
each packet may experience a wait at a switch before it is forwarded.
Delay is not uniform as not all packets pass through same switches.
Considering the figure,
There are three transmission times (3T), three propagation delays (slopes 3 of the lines), and two waiting times (w1 + w2).
We ignore the processing time in each switch.
Total delay = 3T + 3  + w1 + w2

## Slide 21: Issues
Efficiency
The efficiency of a datagram network is better than that of a circuit-switched network;
Resources are allocated only when there are packets to be transferred.
Reallocation is done if there is delay in communication between two devices.

## Slide 22: Virtual Circuit Network
A virtual-circuit network is a cross between a circuit-switched network and a datagram network.
Resources can be allocated during the setup phase, as in a circuit-switched network, or on demand, as in a datagram network.
all packets follow the same path established during the connection.
there are setup and teardown phases in addition to the data transfer phase.
A virtual-circuit network is normally implemented in the data-link layer, while a circuit-switched network is implemented in the physical layer and a datagram network in the network layer.

## Slide 23: Virtual Circuit Network

## Slide 24: Addressing in VCN
In a virtual-circuit network, two types of addressing are involved: global and local (virtual-circuit identifier).
Global – unique in the scope of the network or internationally
global address in virtual-circuit networks is used only to create a virtual-circuit identifier
The identifier that is actually used for data transfer is called the virtual-circuit identifier (VCI) or the label.
It is a small number that has only switch scope; it is used by a frame between two switches.

## Slide 25
When a frame arrives at a switch, it has a VCI; when it leaves, it has a different VCI.

## Slide 26: Three phases
V-Circuit switching requires three phases:
  Setup phase
  Data Transfer phase
  Teardown phase

## Slide 27: Setup phase
the source and destination use their global addresses to help switches make table entries for the connection.

## Slide 28: Data Transfer phase
All switches need to have a table entry for this virtual circuit.
Table has four columns.
The switch holds four pieces of information for each virtual circuit
We assume that each switch has a table with entries for all active virtual circuits.

## Slide 29: Data Transfer phase
data-transfer phase is active until the source sends all its frames to the destination.
Table

## Slide 30: Data Transfer phase

## Slide 31: Setup phase

## Slide 32: Acknowledgment in setup
A special frame, called the acknowledgment frame, completes the entries in the switching tables.

## Slide 33: Teardown phase
In this phase, source A, after sending all frames to B, sends a special frame called a teardown request.
Destination B responds with a teardown confirmation frame. All switches delete the corresponding entry from their tables.

## Slide 34: Delay

## Slide 35: Delay
There are three transmission times (3T ), three propagation times (3), data transfer depicted by the sloping lines, a setup delay (which includes transmission and propagation in two directions), and a teardown delay (which includes transmission and propagation in one direction).

## Slide 36: Efficiency
During setup, the delay for each packet is the same
During data transfer, each packet may encounter different delays
Resource allocation is on demand.The source can check the availability of the resources, without actually reserving it.

## Slide 37: Switching in TCP/IP layers
Physical layer – only circuit switching. No packets exchanged.
Data Link layer - Packet switching at the data-link layer is normally done
using a virtual-circuit approach.
Network layer - packet switching. In this case, either a virtual-circuit approach or a datagram approach can be used.
App. Layer- only message switching. The communication at the application layer occurs by exchanging messages